ANSI Dimensioning Guidelines for Working Drawings

To be turned in with finished set of drawings

- Limit dimensions should be used on all individually dimensioned tolerance parts.

- The Baseline dimensioning system should be used to locate tolerance surfaces to avoid an accumulation of tolerance.

- All dimensions should be given in decimals except drill sizes, fillets and rounds, and standard fasteners.

- Each dimension should be given clearly so that it can be interpreted in only one way.

- Dimensions should not be duplicated or the same information given in two different ways and no dimensions should be given except those needed to produce or inspect the part.

- Dimensions should be given between points or surfaces that have a functional relation to each other or that control the location of mating parts.

- Dimensions should be given to finished surfaces or important center lines, in preference to rough surfaces, whenever possible.

- Dimensions should be so given that it will not be necessary for the machinist to calculate, scale, or assume any dimension.

- Dimensions should be given in the view where the shape is best shown.

- Dimensions should be placed in the views where the features dimensioned are shown true shape.

- Dimensioning to hidden lines should be avoided whenever possible.

- Dimensions should not be placed on a view unless it eliminates long extension lines and makes the dimension clearer.

- Dimensions applying to two adjacent views should be placed between the views if possible.

- The longer dimensions should be placed outside all intermediate dimensions so that dimension lines will not cross extension lines.

- In machine drawing, all inch marks are omitted unless necessary.

- Do not force workers to assume that a feature is centered. Provide a location dimension.

- Non-toleranced detail dimensions may be chained if necessary.

- Avoid a complete chain of detail dimensions by omitting one and providing an overall dimension.

- Dimension lines should be spaced uniformly approximately 3/8” apart.

- No line of the drawing should be used as a dimension line or coincide with a dimension line.

- A dimension line should never be joined end to end with any line of the drawing.

- Dimension lines should not cross if it can be avoided.

- Extension lines should not cross dimension lines except for angled leaders.

- Extension lines may cross other extension lines.

- Center lines may be extended and used as extension lines.

- Center lines should not extend from view to view.

- Leaders for notes should point to the center of circular views of holes whenever possible.

- Leaders should not be horizontal or vertical.

- Dimension figures should never be crowded or difficult to read.

- Notes should be brief and clear and the wording should be standard in form.

- Finish marks should be placed on the edge views of all finished surfaces, including hidden edges and the contour and circular views of cylindrical surfaces.

- Finish marks should be omitted on holes or other features where a note specifies a machining operation.

- Finish marks should be omitted on parts made from rolled stock.

- If a part is finished all over, all finish marks should be omitted, and the general note FAO or FINISH ALL OVER should be used.

- Cylinders are normally dimensioned by giving both their diameter and length in the rectangular view, except when notes are used for holes. A diameter in the circular view may be used in cases where it is clearer.

- In general, a circle is dimensioned as a diameter and an arc is dimensioned as a radius.

- A diameter dimension should always be preceded by the symbol Æ.

- The letter R should always precede a radius dimension. The arrowhead should pass through or point through the arc center and touch the arc.

- Cylinders and holes should be located by their center lines in the circular view if possible.

- Where there are several rough, non-critical features that are obviously the same size (fillets,rounds, ribs, etc.), only one dimension is needed and may be given as a note or followed with the abbreviation TYP standing for typical.

- Mating dimensions should be given correspondingly on drawings of mating parts.